## Slide 1
LAN Considerations

## Slide 2: Overview
Enclave LAN Core
  Core Distribution and access layer
  Installing lan
  Vlans
  Dhcp
  ssh
Notes: 1. Design
2. VLANs
3. STP
4. VLAN Pruning
5. Router on a stick / Inter-VLAN Routing
6. DHCP
7. Login
8. remote management
9. Port Security
10. ACLs

## Slide 3: The hierarchical internetworking model defined by cisco includes a core layer, distribution layer and access layer. Network switches working within these layers get corresponding names

## Slide 4
CORE switch
  The core switch is the network switch that I positioned the backbone or physical core of a network.
  It will serve as the gateway to a wan or the internet.
Distribution switch
  The distribution switch links upwards to the core switch and downwards to the access switch.
  It functions as a bridge and ensures that packets are appropriately routed between subnets and VLANs in an enterprise network.
Access switch
  Located in that access layer, an access switch is used to connect majority od devices to a network.
  Mostly used in offices and server rooms and will usually have high-density ports (48 port sw).

## Slide 5: Installing a local area network
When installing a lan there are 7 steps to consider
  Identify gear you will need to set up the network
    Servers, routers, switches etc
  Configure the wan on the router
    Interfaces, tunnels, vlans, routing protocols, dhcp, ssh
  Configure lan ports on router and switches
    trunk and access ports, ssh
  Identify to local services you need available on the network
    (user, voice, print, video etc)
  Identify how many devices will be connecting to the network (Laptops, phones, vtc’s etc)
  Run cables to all workstations/ end devices
    if possible use jumper cables from phones to laptops
  Test all services and internet connectivity.
    Ensure to verify internet on each end device, make internal and external phone calls on each phone/ vtc, and print test pages on every printer.

## Slide 6: Virtual Local Area Network (VLAN)

## Slide 7: VLAN
A LAN is a broadcast domain operating at Layer 2 in the OSI model. Host within this LAN will share common network space and can only communicate within the LAN.
VLANs allow network administrators to logically segment a LAN into different broadcast domains.
Since VLANs operate at the data link layer, a Layer 3 device is required for a local device to communicate with a device outside of its local network space.

## Slide 8: Functionality of VLANs
Each VLAN will apply a tag to an incoming network frames, allowing for traffic to broadcast to only interfaces where this tag is applied.
*Picture*
VLANs are numbered and range from 1 – 4096.
By default, VLAN 1 applied to all interfaces.
VLAN 1, 1002, 1003, 1004 and 1005 are default created in the VLAN database.

## Slide 9: Configuring VLANs
A VLAN can be created one of two ways.
  Under the global config mode.
    Switch(config)#vlan 10
    Switch(config-vlan)#name Test
      A VLAN is not created until you exit config-vlan or create next VLAN.
  Under a switchport interface.
    Switch(config)#interface FastEthernet 0/12
    Switch(config-if)#switchport access vlan 20
      % Access VLAN does not exist. Creating vlan 20

## Slide 10: Verifying VLANs
Show VLAN brief
Switch#show vlan brief
VLAN Name Status Ports
---- ------------------------------- ---------- -------------------------------
1 default active Fa0/1, Fa0/2, Fa0/3
Fa0/4, Fa0/5, Fa0/6
Fa0/7, Fa0/8, Fa0/9
Fa0/10, Fa0/11
10 Test active
20 VLAN0020 active Fe0/12
1002 fddi-default act/unsup
1003 trcrf-default act/unsup
1004 fddinet-default act/unsup
1005 trbrf-default act/unsup

## Slide 11: QUESTION
True or False- VLANs allow network administrators to logically segment a LAN into different broadcast domains.
Answer:
  True

## Slide 12: Dynamic Host Control Protocol (DHCP)

## Slide 13: Dynamic Host Control Protocol (DHCP)
DHCP is commonly used for assigning IPv4 address information to a network host. DHCP allows a DHCP client to obtain an IP address, subnet mask, default gateway IP address, DNS server IP address, and other type of IP addressing information from a DHCP server.

## Slide 14: The DORA process
  DHCP Discover
    A broadcast message is sent out to see if there is a DHCP server available
  DHCP Offer
    A DHCP server will see/receive the message and respond with an OFFER that has an unreleased IP address, subnet mask, and default gateway
  DHCP Request
    The client responds to the OFFER message with this type of message saying that it will accept the contents of the OFFER message
  DHCP Acknowledge
    The server sends this message acknowledging that the IP has been accepted and is spoken for. At this time any other items like lease duration is negotiated.

## Slide 15: DHCP Server Configuration
  Configure terminal
  IP dhcp pool "desired pool name"
  Network pool x.x.x.x y.y.y.y (VLAN Network)
    Creates a pool of addresses that the server will assign IP addresses from
  Default-router x.x.x.x (Interface VLAN IP)
  Dns server x.x.x.x (primary) x.x.x.x (alternate)
  IP dhcp excluded-address x.x.x.x x.x.x.x
  Domain-name (domain that you are operating on)
  FOR VOICE NETWORK ONLY
  Option 150
  Ip x.x.x.x (call manager IP)

## Slide 16: Verifying DHCP on a client
  Open cmd
  Ipconfig /all
  Ensure DHCP is yes, autoconfiguration enabled is yes, and there is an IP address in autoconfiguration IP address
  If an ip does not populate
    Ipconfig /release
    Ipconfig /renew

## Slide 17: Troubleshooting DHCP
  Show ip dhcp conflict
    This will show if there is a conflict with an IP address
  Clear ip DHCP conflict
    This will clear the assigned IP address and start the DORA proccess over
  Show ip dhcp binding
  Clear ip dhcp binding

## Slide 18: Secure Shell

## Slide 19: SSH
The Secure Shell Protocol (SSH) is a cryptographic network protocol for operating network services securely over an unsecured network.[1] Its most notable applications are remote login sessions between an authorized user and a trusted host over the internet.
SSH service was created as a secure replacement for the unencrypted Telnet and uses cryptographic techniques to ensure that all communication to and from the remote server happens in an encrypted manner.
SSH-1 refers to any implementation of the first version of the SSH protocol.
SSH-2 refers to any implementation of the second version of the SSH protocol
When comparing SSH2 to SSH1, it's important to note that SSH2 is not simply SSH1 with new protocols plugged in. It's a complete rewrite of the original protocol that incorporates built-in protections against known vulnerabilities in SSH1.

## Slide 20: Differences between SSH and SSH2
The major differences between SSH1 and SSH2 fall into two main categories: technical and licensing. SSH2 uses different encryption and authentication algorithms. SSH1 supported four encryption algorithms, two of which had been found to be unsecure.
SSH1 symmetric key block encryption algorithms included the following:
  Data Encryption Standard (DES), Triple DES, The International Data Encryption Algorithm (IDEA), and blowfish
SSH2 dropped support for DES and IDEA encryption algorithms because they were found to be subject to successful attacks. SSH2 currently supports the following encryption algorithms:
AES, Blowfish, 3DES, CAST-128, Rivest Cipher 4 (RC4)

## Slide 21: Differences cont.
SSH1 used the RSA authentication algorithm, SSH2 switched to the Digital Signature Algorithm, or DSA. These changes were designed to both circumvent intellectual property issues surrounding the use of IDEA and RSA and increase the base level of security in SSH2 by using stronger algorithms for the exchange of host keys and password authentication.
SSH2 also provides added functionality. Most notably, it adds the secure file transfer protocol, or sftp, program to the SSH suite. This program uses the SSH protocol's transport layer encryption technology to provide a secure means for file transfer between remote systems.

## Slide 22: How Does SSH Work
Utilizing Windows, you will need to utilize an SSH client to open SSH connections. The more popular SSH clients are PuTTY or SecutrCRT
The protocol works in the client-server model, which means that the connection is established by the SSH client connecting to the SSH server. The SSH client drives the connection setup process and uses public key cryptography to verify the identity of the SSH server. After the setup phase the SSH protocol uses strong symmetric encryption and hashing algorithms to ensure the privacy and integrity of the data that is exchanged between the client and server.

## Slide 23: SSH requirements
requirements for SSH2
  Ip domain name
  Reachable ip on a device
  Loopback int (typically /32 or IP on management network)
  Crypto key (A-symetric encryption algorithm preferably rsa)
  SSH 2 enabled
  Username and password
  Line con 0 configurations
  Line vty 0 15 configurations

## Slide 24: SSH configurations
Ip domain name XXX (domain name)
Int loopback 1 (needs to be advertised if its on a connected network)
  Ip add x.x.x.x x.x.x.x
Crypto key generate rsa module 2048 (A-symetric encryption algorithm)
Ip ssh version 2 (creates ssh)
Username (admin) priv 15 algorithmic-type script secret (admin)
Username (admin) priv 5 algorithmic-type script secret (admin)
L ine con 0
  Login local
  Transport proffered ssh
  Transport intput ssh
  Transport output ssh
Line vty 0 15
  Login local
  Transport proffered ssh
  Transport intput ssh
  Transport output ssh
To Verify if SSH works
  On any switch, router our laptop within you LAN and WAN , on putty secure crt or command prompt type the following
    ssh –l x.x.x.x (Username) (Password)

## Slide 25: Router On A Stick

## Slide 26: Router On A Stick
Router-on-a-stick (ROAS) is a feature that allows us to route packets to subnets associated with VLANs connected to a router 802.1Q trunk. It uses a router VLAN trunking configuration to give the router a logical interface connected to each VLAN.

## Slide 27: Router cONFIGURATIONS
Router Config
  Int g2/0.x (whatever outbound interface you are routing through, it is good practice to associate your subinterface to your vlan baing created. Ex: G2/0.30 for vlan 30)
  Encapsilation dot1q (vlan ID)
  Ip address x.x.x.x x.x.x.x (ip address and subnet mask of your network associated to your vlan)
  Description (brief description of vlan)
  Route your vlan traffic
  Router EIGRP (AS number)
  Network x.x.x.x x.x.x.x(broadcast your vlan networks ensure you do not broadcast your nbma network (pt net/outside interface) )

## Slide 28: NETWORK MODULE ENHANCE(nme) Configurations
Switch/NME config
  Access NME through router
    Service-module gigabitethernet g2/0 session
    To exit back to router: (Ctrl+Shift 6) x
  Ensure that your connection from router to switch is set to trunk
    Int range g0/25-26
    Switchport trunk encapsulation dot1q
    Switchprot mode trunk (this establishes the connection from the router to the NME)
  Configure VLANs to interfaces
    Vlan xx
    Name (user/voice/print etc)
    exit
    Int g1/0/x (interface you want to add vlan to)
    Switchport mode access
    Switchport access vlan xx(vlan you want to assign)
    Switchport access voice vlan xx (voice vlan; only voice and user VLANs can be added to the same interface)

## Slide 29: questions