## Slide 1: Basic Networking Configuration Commands

## Slide 2
BASIC L2 SWITCH CONFIGS
Change hostname
switch(config)#hostname access
access(config)#
Set clock time
access#clock set 3:03:14 October 09 2022
Set username and password
access(config)#username jesus.ortiz priv 15 algorythimic-type scrypt secret (password)
access(config)#line con 0
access(config-line)#login local
Prevent message interruptions
accesss(config)#line con 0
access(config-line)# logging synchronous
switch>en
Switch# conf t

## Slide 3
BASIC L2 SWITCH CONFIGS
Save configurations
Re-upload saved configurations
access#copy run start/ accesss (config)# do copy run start
Erase configurations
access#write erase / accesss (config)# do wr era
Create vlans
access(config)#vlan 5
access(config-vlan)# name ***KG***
access#write memory / access(config)# do wr mem
access#copy start run / access (config)# do copy start run
access#reload / accesss (config)# do reload
access(config-vlan)# exit

## Slide 4
BASIC L2 SWITCH CONFIGS
Create interface vlans
Create access ports
access(config)# ing g0/1
Create trunk ports
access(config)# ing g0/1
Configure IP’s
access(config)# ing g0/1
access(config)#int vlan 5
access(config-vlan)# desc***KG***
access(config-vlan)# ip add 10.20.30.1 255.255.255.0
access(config-vlan)# exit
access(config-int)# switchport mode access
access(config-int)#switchport acces vlan 5
access(config-int)# switchport trunk encapsulation dot1q
access(config-int)# switchport mode trunk
Optional (must match on both ends
access(config-int)# switchport trunk allowed vlan (all , 5)
access(config-int)# no switchport
access(config-int)# ip add 10.20.30.1 255.255.255.0

## Slide 5
BASIC L2 SWITCH CONFIGS
See connected devices
Check interface types/connected interfaces
access#sho ip interface brief / access(config)#sho ip int brie
Check configurations
access#show running configuration / accesss (config)# do sho run
Check routing table
access#sho ip route/ access(config)#do sho ip route
access#show cdp neighbors/ access(config)# do sho cdp neigh

## Slide 6
BASIC L3 SWITCH CONFIGS
Change from L2-L3 switch:
Configure eigrp
access(config)# router eigrp 10
Configure IP Route
access(config)#ip route 10.10.10.0 255.255.255.248 10.20.30.2
Configure Router Rip
access(config)# router rip
access(config)#ip routing
access(config-router)# network 10.20.30.0 0.0.0.3
access(config-router)# no auto summary
access(config-router)# network 10.0.0.0
access(config-router)# version 2
(network you want to reach) (network subnet)(your next hop)
access(config-router)# no auto-summary

## Slide 7
BASIC L3 SWITCH CONFIGS
How to ping
How to trace route
Access#traceroute 10.20.30.1 / access(config)#do traceroute 10.20.30.1
Access#ping 10.20.30.1 / access(config)#do ping 10.20.30.1

## Slide 8
BASIC ROUTER CONFIGS
Change hostname
router(config)#hostname black_core
black_core(config)#
Set clock time
black_core#clock set 3:03:14 October 09 2022
Set username and password
black_core(config)#username jesus.ortiz priv 15 algorythimic-type scrypt secret (password)
black_core(config)#line con 0
black_core(config-line)#login local
Prevent message interruptions
black_core(config)#line con 0
black_core(config-line)# logging synchronous
router>en
router# conf t

## Slide 9
BASIC ROUTER CONFIGS
Save configurations
Re-upload saved configurations
black_core#copy run start/ accesss (config)# do copy run start
Erase configurations
black_core#write erase / accesss (config)# do wr era
Create vlans
black_core(config)#vlan 5
black_core(config-vlan)# name ***KG***
black_core#write memory / access(config)# do wr mem
black_core#copy start run / access (config)# do copy start run
black_core#reload / accesss (config)# do reload
black_core(config-vlan)# exit

## Slide 10
BASIC ROUTER CONFIGS
Create interface vlans
Configure an interface
black_core(config)# int g0/1
Create a tunnel
black_core(config)# int tunnel 100
Configure IP’s
black_coreconfig)# ing g0/1
black_core(config)#int vlan 5
black_core(config-vlan)# desc***KG***
black_core(config-vlan)# ip add 10.20.30.1 255.255.255.0
black_core(config-vlan)# exit
black_core(config-if)# ip add 10.20.30.1 255.255.255.0
black_cores(config-if)#desc ***DKET***
black_core(config-if)# no switchport
black_core(config-if)# ip add 10.20.30.1 255.255.255.0

## Slide 11
Tips and Tricks
Up arrow
Tab
Tab will finish words that you are typing
?
? Will show you commands that you can type and or show you the next part of the command.
Ctrl commands
Ctrl a – brings you to the beginning of the command line
The up arrow will allow you to bring up previous commands that you typed
Ctrl e – brings you to the end of the command line
Ctrl u – deletes entire command lines behind curser .
Ctrl w – deletes words behind curser

## Slide 12
Tips and Tricks
Break (|)
When trouble shooting you may hear some one say “do sho run Break b router” or do sho run break s Crypto
What this means is you can specify when in the running configurations that you want to be taken to with “B” meaning beginning and “S” meaning Section. The commands looks like this
router# sho run | b router eirgrp
router(config)# do sho run | s crypto

## Slide 13
BASIC TROUBLE SHOOTING STEPS
LAYER 1
Show Run
Doing a show run to validate that everything needed is configured and not fat fingered should be one of the first things you do after finishing configs
Tunnel.
“sho run int tun 100” - to check all the tunnel configs
Always check the physical layer 1st before going down a rabbit hole
“sho run all int tun 100” - If some configs don’t show
“sho dmvpn” To check if your tunnel is up
“clear dmvpn session” – to restart the tunnel after trouble shooting.
“shut / no shut” – turn tunnel off and on after making changes

## Slide 14
BASIC TROUBLE SHOOTING STEPS
EIGRP
Crypto
“sho run | s crypto” - takes you to crypto section and only shows what you have configured
Interface’s
“sho run int g0/0/ or fa0/1” - takes you to only that interface.
“sho run | s eigrp” - takes you to eigrp section and only shows what you have advertised
“sho ip eigrp neighbors” – lets you know if you have an adjacency with CBS
“sho crypto isakmp sa” – shows you if you have a security association should be qm idle
“Clear crypot sa” – resets youre security association
“Clear crypot isakmp” resets isakmp.
“default int g0/0” - resets the interface to default commands